## Slide 1: BigBuild: Light Frame Wood Shear Walls
An explainable shear-wall design tool for the NCSEA Big Build Hackathon

## Slide 2: The project
Engineers designing multi-story multifamily buildings often work through shear-wall stacks with hand calculations and spreadsheets.
We want to explore a Python app that makes those calculations visible, checks individual components, and shows how design assumptions affect the results.
Prototype only: results need validation against selected references and engineering review before project use.

## Slide 3: Hackathon goal
A Python prototype for one five-story stack of vertically aligned, solid wood structural panel (WSP) shear walls without openings
Start from applied seismic story loads
Show component-by-component checks and calculated story drift
Make every result traceable: inputs, units, assumptions, intermediate results, and reference citations
Components: sheathing, boundary studs/posts in compression and tension, hold-downs or continuous tie-downs, and stack connections

## Slide 4: Interactive Shear Wall Design
Plan view with tributary zones and holdowns
Free-body diagram with story inputs and results

## Slide 5: Interactive Shear Wall Design, continued
Wall schedule, holdown table and assembly catalog
Aligned two-story stack with accumulated overturning

## Slide 6: Engineering basis
Standards: IBC 2024, SDPWS 2021, NDS 2024, ASCE 7-22; CBC is out of scope
Edition differences between a worked example and this basis are recorded, never silently treated as equivalent
OpenSeesPy is an installed candidate engine; it does not supply wood design provisions
Decided at the event: wall idealization, load conventions, boundary conditions, drift treatment, component checks, and acceptance tolerances

## Slide 7: Reference examples
WoodWorks five-story light-frame wood structure over podium (2nd ed., Nov 2025): §3.3 shear wall design and §3.4 drift are the candidate benchmark starting point
WoodWorks cantilever wood diaphragm (updated May 2026): wall stiffness, rigid diaphragm force distribution, and drift context; not a five-story benchmark
Both PDFs are in the repo with the owner's confirmation of distribution permission
Licensed standards stay outside the repository

## Slide 8: How the repository is organized
src/analysis/ structural model and response calculations
src/design/ component checks and reported calculation steps
src/ui/ user interface; Streamlit is available
tests/ engineering benchmarks and regression tests
references/public/ documents with confirmed redistribution permission
tools/ generic environment verification
No application code or engineering benchmark exists yet; it is built at the event

## Slide 9: Team
Scott Breneman
Project owner
Dago DeLaRosa
Samantha Joyce
Alex Bonnar
Vince LaCoste
Sam Martin

## Slide 10: Team, continued
Aidan Anderson
Hamid Khodadadi
Garret Mills
Miles Bennet

## Slide 11: Project Links
BigBuild-LFW-Shearwalls
GitHub repository
github.com/scottbreneman/BigBuild-LFW-Shearwalls